## Slide 1
TerraFlood
Flood extent mapping
Lisa Landuyt
Jurgen Everaerts
Eurisy Satellite-based Services for Disaster Risk Management
Brussels 11 December 2023

## Slide 3
Sentinel-1 RADAR (SAR)
to the rescue

## Slide 4: What is so great/bad about Sentinel-1?
RADAR is not much affected by clouds
Active system, does not require sunlight
Systematic coverage (every x days)
Operations to continue for many years to come
Image resolution ~ 10m
Noisy images
Clutter

## Slide 5: Interpreting a SAR backscatter image
Scattering mechanism
Image tone
specular
reflection
corner
reflection
diffuse
scattering
volume
scattering

## Slide 6: All Sentinel-1 observations since 2015

## Slide 7: Fluvial flood risk map

## Slide 8: TerraFlood algorithm
Pixel-based approach
Thresholding
Region growing
Edge refinement
Object-based approach
Thresholding
Region growing
Edge refinement
Combination pixel- and object-based approach
Final flood map
(8 classes)
SAR
image pair
Land Cover
Elevation
Flood Risk
Flood Depth
More info:
L. Landuyt, F. M. B. Van Coillie, B. Vogels, J. Dewelde and N. E. C. Verhoest, "Towards Operational Flood Monitoring in Flanders Using Sentinel-1," in IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, vol. 14, pp. 11004-11018, 2021, doi: 10.1109/JSTARS.2021.3121992.
Notes: We chose for a dual approach, making use of the advantages of both the pixel and the object level. We start from thresholding, as this very fast, but combine it with several refinements based on region growing and edge refinement.
As I said, we chose to fully exploit the local data availability. Besides SAR, we also use land cover, elevation and flood risk elevation.
Moreover, we make use of a SAR pair, in order to discriminate between permanent and temporary water surfaces.
All of this results in an 8-class map, discriminating …
Flood water beneath trees cannot be seen using C-band SAR, but making use of our ancillary data we are able to proved a “probably flooded forest” class.
We tested and validated our approach based on a set of drone images. If you want to know more, we described everything in detail in a paper.

## Slide 9: Derived products
Maximum flood extent
Flood duration
Flood recurrence

## Slide 10: TerraFlood products: NRT maps
Notes: This algorithm allowed us to translate VMM’s water level time series into spatial maps, as you can see here for the floods in the Demer valley in July 2021.
You can see lake Schulensbroek, a permanent water body.
Its surroundings are used a retention basin to protect the nearby cities from flooding. As you can see, the retention basin was successfully activated in the beginning of the month, and then emptied in time to buffer the mid-July peak. Then also many agricultural areas got flooded.

## Slide 11: Need more detail? Sentinel-1 vs Capella Space

## Slide 12: Capella space example